RANCID exercises

AfNOG 11, Kigali

RANCID and CVSWeb are already installed on your stations - on a clean Ubuntu you can install them with:

sudo apt-get install rancid-core rancid-util expect cvsweb

(you need a webserver installed like apache2)

Choose your assigned router:

PC1-10: 196.200.218.249
PC11-20: 196.200.218.250
PC21-28: 196.200.218.251

PC29-36: 196.200.218.252

PC37-44: 196.200.218.253

You will monitor all routers, but only make changes in your group for the assigned router

- RANCID will run as the rancid user on the local workstation. So will this exercise

  - Login as root first: su (use password on the board)

  - Login as user rancid: su -s /bin/bash rancid

  - Change to the home directory of rancid: cd ~

  - Check: pwd - you should be in /var/lib/rancid

- First you need to configure clogin so it can login to the routers

  - Login to your assigned router via telnet, enter configuration mode and add a user rancid. :
ssh inst@x.x.x.x (use your assigned router ip - enter the password)

  - Enter the following commands on the router command line:
conf t
username rancid password rancid
end
wr
exit

  - vi .cloginrc (or use your favourite editor). Enter the following file:

add user * rancid

add password * {rancid} {afnog}

(This tells rancid it can login to all routers via telnet with username rancid, password rancid and enable password AfNOG - if you want usernames/passwords per router, just put the IP address instead of * and use one line per router)

  - Protect the file from other users: chmod 600 .cloginrc

  - Try it with your assigned router: bin/clogin x.x.x.x --- you should be automatically logged in. exit the router (if it doesn't work try again - there can only by 5 at the same time)

- You need to define the groups of devices - we will only have one called cisco (you could have one for each Cisco,HP,Juniper, one per city, per workgroup, whatever):

  - Open a new terminal window, you need to be root.  Do
sudo vi /etc/rancid/rancid.conf (use vi or your favourite editor, but you must be root)

  - search for the line LIST_OF_GROUPS, uncomment it and set only one group "all". It should look like this:
LIST_OF_GROUPS="all"

  - Save and exit the editor

  - Before you continue, make sure you are user rancid again (run whoami to confirm). Run su -s /bin/bash rancid if you are not.

  - Let rancid create necessary files. Run /var/lib/rancid/bin/rancid-cvs. You should see output like this:
No conflicts created by this import

cvs checkout: Updating all
Directory /var/lib/rancid/CVS/all/configs added to the repository
cvs commit: Examining configs
cvs add: scheduling file `router.db' for addition
cvs add: use `cvs commit' to add this file permanently
/var/lib/rancid/CVS/all/router.db,v  <--  router.db
initial revision: 1.1

- Now add the monitored routers to the router.db file of the group.

  - Edit /var/lib/rancid/all/router.db

  - Add one line like this for every router in the classroom (monitor all of them, not only your assigned one):
196.200.218.249:cisco:up
196.200.218.250:cisco:up
196.200.218.251:cisco:up
196.200.218.252:cisco:up
196.200.218.253:cisco:up

  - Save the file and exit

- Check that someone in each row has at least completed Step 2, so your rancid will be able to login to all routers in the classroom

- Run rancid the first time

  - /var/lib/rancid/bin/rancid-run

  - Check the logs: more /var/lib/rancid/logs/*

  - If it looks ok you should be able to see all router configuration files with ls cisco/configs - check one:
more /var/lib/rancid/all/configs/x.x.x.x

- Now change something on your assigned router:

  - bin/clogin x.x.x.x (this should still work)

  - conf t

  - Change something on the router which has no effect according to the following schema:

    - PC 1,11,21,29,37: snmp-server location <YOUR HOMETOWN and Country>

    - PC 2,12,22,30,38: snmp-server contact <Name of someone in class>

    - PC 3,13,23,31,39,: banner motd ^ AfNOG is cool!!! ^

    - PC 4,14,24,32,40: access-list 1337 permit any

    - PC 5,15,25,33,41: interface Loopback 0
          description My home is my castle

    - PC 6,16,26,34,42: line vty 0 4
          logout-warning 60

    - PC 7,17,27,35,43: line vty 0 4
                      motd-banner

    - PC 8,18,28,36,44: no ip httpd server

    - PC 9,19: service nagle

    - PC 10,20: autonomous-system 65432

  - end

  - wr

  - exit

- Run rancid again

  - /var/lib/rancid/bin/rancid-run

  - Check /var/lib/rancid/all/configs/x.x.x.x - can you spot your change?

  - Look at other files, did they change? How can you tell?

  - cd /var/lib/rancid/all/configs

  - try cvs log x.x.x.x for files you suspect changed to see revisions, then cvs diff -r1.3 -r1.2 x.x.x.x (or similar) to compare revisions (or cvs annotate x.x.x.x)

  - feel free to run rancid again to catch other people's changes.

- Now add the  switches from the network diagram:

  - Edit /var/lib/rancid/all/router.db

  - Add one line like this for every Cisco switch in the classroom (2 are Cisco, 3 are HP):
196.200.218.29:cisco:up
196.200.218.61:cisco:up

  - Run bin/rancid-run again and look at the changes

- Look at your configs via Web Interface

  - Edit (as root) /etc/cvsweb/cvsweb.conf

  - search for /var/lib/cvs and change to /var/lib/rancid/CVS, save and exit

  - make a link to cvsweb: sudo ln -s /usr/share/cvsweb /var/www/cvsweb

  - Open in your browser: http://localhost/cgi-bin/cvsweb - and navigate there
Obviously, if you choose to use this "at home", secure that web server

- Bonus exercise if you're done early: Add mail capabilites to RANCID:

  - Edit /etc/aliases as root and insert the following:
rancid-all: net@noc.mgmt.ws.afnog.org
rancid-admin-all: net@noc.mgmt.ws.afnog.org

  - Then run 'newaliases'

This will forward all rancid emails to the RT on the NOC maching

  - Change the snmp location to something else (see step 7)

  - Run /var/lib/rancid/bin/rancid-run again

  - You should have mail in RT showing the changes